Router Commandoer

enable

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| enable | To enter the privileged EXEC mode, use the enable command in User EXEC mode. | enable [ privilege-level ] |

exit

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| exit | Use the exit command in User EXEC mode or privileged EXEC mode to log off the router. This process is also called exiting the active session or exiting from the EXEC process. | exit |

?

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| ? | To display a brief description of the help system, enter the help command. | ? |

disable

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| disable | To exit privileged EXEC mode and return to user EXEC mode, or to exit to a lower privilege level, enter the disable command in EXEC mode. | disable [ privilege-level ] |

show version

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| show version | To display information about the currently loaded software version along with hardware and device information, use the show version command in EXEC mode. | show version |

show flash

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| show flash | To display the layout and contents of a Flash memory file system, use the show flash command in EXEC mode. | for Class A Flash file systems: show flash-filesystem : [ all ¦ chips ¦ filesys ] for Class B Flash file systems: show flash-filesystem : [ partition number ] [ all ¦ chips ¦ detailed ¦ err ¦ summary ] for Class C Flash file systems: show flash-filesystem : for all Flash file systems: show flash is an acceptable, informative usage |

copy tftp flash

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| copy tftp flash | To copy an IOS image stored on a TFTP server into the flash memory of the router, use the copy tftp flash command in EXEC mode. | copy tftp { file-id ¦ flash ¦ config } |

setup

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| setup | To enter the Setup Command Facility, use the setup command in privileged EXEC mode. Setup mode gives the option of configuring a router without using the Cisco IOS Command Line Interface (CLI). Setup provides a high-level view of the configuration and guides the user through a basic configuration process. If a user is not familiar with the CLI, Setup mode is a valuable tool because it prompts for specific information required to configure a router. | setup |

enable secret

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| enable secret | To specify an additional layer of security over the enable password command, use the enable secret command in global configuration mode. It is recommended that the enable secret password always be set and used because it is encrypted while the enable password is not encrypted. | enable secret [ level level ] { password ¦ [ encryption-type ] encrypted-password } |

enable password

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| enable password | To set a local password to control access to various privilege levels, use the enable password command in global configuration mode. | enable password [ level level ] { password ¦ [ encryption-type ] encrypted-password } |

clock set

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| clock set | To manually set the system software clock, use one of the formats of the clock set command in privileged EXEC mode. | clock set hh:mm:ss day month year clock set hh:mm:ss month day year |

Ctrl-P

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Ctrl-P | To recall commands in the history buffer beginning with the most recent command, press Ctrl-P or the up arrow key repeatedly to recall successively older commands. | Ctrl-P |

terminal editing

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| terminal editing | To reenable the enhanced editing mode for only the current terminal session, use the terminal editing command in EXEC mode. Enhanced editing mode is automatically enabled with the current IOS software release. | terminal editing |

terminal no editing

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| terminal no editing | To disable the enhanced editing mode on the current line, use the no terminal editing command in EXEC mode. Enhanced editing mode can be disabled if it interferes with the interaction of written scripts. | terminal no editing |

Ctrl-A

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Ctrl-A | Ctrl-A will return a user directly to the beginning of the command line. | Ctrl-A |

Esc-B

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Esc-B | Esc-B will allow a user to scroll back on the command line one word at a time. | Esc-B |

Ctrl-B

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Ctrl-B | To scroll back on the command line one character at a time, press Ctrl-B or the left arrow key repeatedly until the beginning of the command entry is reached. | Ctrl-B |

Ctrl-E

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Ctrl-E | Ctrl-E will move a user directly to the end of the command line. | Ctrl-E |

Ctrl-F

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Ctrl-F | To scroll forward on the command line one character at a time, press Ctrl-F or the right arrow key repeatedly until the end of the command entry is reached. | Ctrl-F |

Esc-F

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Esc-F | Esc-F will allow a user to move forward on the command line one word at a time. | Esc-F |

Ctrl-Z

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Ctrl-Z | To return to the privileged EXEC mode from the global configuration mode, type Ctrl-Z. Ctrl-Z may also be used to return directly to the privileged EXEC mode from any sub-mode of global configuration mode. | Ctrl-Z |

terminal history size

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| terminal history size | To change the size of the command history buffer for the current terminal session, use the terminal history size command in EXEC mode. The number-of-lines range is from 0 to 256. The default is 10. To reset the command history buffer to its default size of 10 lines, use the no form of this command. | terminal history size number-of-lines |

history size

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| history size | To change the command history buffer size for a particular line, use the history size command in line configuration mode. The number-of-lines range is from 0 to 256. The default is 10. To reset the command history buffer to its default size of 10 lines, use the no form of this command. | history size number-of-lines |

Ctrl-N

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Ctrl-N | To return to more recent commands in the history buffer, after recalling commands with Ctrl-P or the up arrow, press Ctrl-N or the down arrow key repeatedly to recall successively more recent commands. | Ctrl-N |

Tab

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| Tab | With the IOS auto-completion feature, the router interface will complete commands for the user if the user enters enough of a command or parameter to make it unique. After entering the unique characters, press the Tab key, to finish the entry. | Tab |

show running-config

| Command | Command Description | Command Syntax |
| --- | --- | --- |
| show running-config | To display the contents of the currently running configuration file or the configuration for a specific interface, or map class information, use the show running-config command in privileged EXEC mode. | show running-config |

configure terminal

Command Command Description Command Syntax configure terminal To enter global configuration mode, use the configure terminal command in privileged EXEC mode. configure terminal

hostname

Command Command Description Command Syntax hostname To specify or modify the host name for a router, use the hostname command in global configuration mode. hostname hostname

router rip

Command Command Description Command Syntax router rip To configure the Routing Information Protocol (RIP) routing process, use the router rip global configuration command. router rip

interface serial 0

Command Command Description Command Syntax interface serial 0 To configure a serial interface on a router, enable the serial interface by using the interface serial command in global configuration mode. interface type number

line console 0

Command Command Description Command Syntax line console 0 To identify a specific line for configuration and begin the line configuration command mode, use the line console configuration command in global configuration mode. Entering the line console command with the optional line type (aux, console , tty , or vty ), designates the line number as a relative line number. Relative line numbers always begin numbering at zero and define the type of line. line [aux ¦ console ¦ tty ¦ vty ] line-number [ ending-line-number ]

password

Command Command Description Command Syntax password To specify a password on a line, use the password command in line configuration mode. The first character cannot be a number. The string can contain any alphanumeric characters, including spaces, up to 80 characters. You cannot specify the password in the format number-space-anything. The space after the number causes problems. For example, hello 21 is a legal password, but 21 hello is not. The password is case sensitive. For example, the password Secret is different than the password secret. To remove the password, use the no form of this command. password password

login

Command Command Description Command Syntax login To enable password checking at login, use the login command in line configuration mode. To disable password checking and allow connections without a password, use the no form of this command. login [local ¦ tacacs]

line vty 0 4

Command Command Description Command Syntax line vty 0 4 The line vty command is used to set the password on the VTY lines. A password must be set on one or more of the virtual terminal (VTY) lines for users to gain remote access to the router using Telnet. Typically, Cisco routers support five VTY lines numbered 0 through 4. line [aux ¦ console ¦ tty ¦ vty ] line-number [ ending-line-number ]

show startup-config

Command Command Description Command Syntax show startup-config The show startup-config command displays the contents of NVRAM, if present and valid, or it shows the configuration file pointed to by the CONFIG_FILE environment variable. show startup-config

service password-encryption

Command Command Description Command Syntax service password-encryption To encrypt passwords, use the service password-encryption command in global configuration mode. This command does not provide a high level of network security. It is primarily useful for keeping unauthorized individuals from viewing the password in the configuration file. service password-encryption

show ?

Command Command Description Command Syntax show ? The command show ? provides a list of available show commands. show ?

show interfaces

Command Command Description Command Syntax show interfaces To display statistics for all interfaces configured on the router or access server, use the show interfaces command in privileged EXEC mode. show interfaces { type number }

show interfaces serial 0/1

Command Command Description Command Syntax show interfaces serial 0/1 To display information about a serial interface, use the show interfaces serial command in privileged EXEC mode. show interfaces { type number }

show controllers serial

Command Command Description Command Syntax show controllers serial Use the show controllers serial privileged EXEC command to display information that is specific to the interface hardware. show controllers serial [ slot/port ]

show hosts

Command Command Description Command Syntax show hosts To display the default domain name, the style of name lookup service, a list of name server hosts, and the cached list of host names and addresses, use the show hosts command in EXEC mode. show hosts

show clock

Command Command Description Command Syntax show clock To display the time and date from the system software clock, use the show clock command in EXEC mode. show clock

show users

Command Command Description Command Syntax show users To display information about the active lines on the router, use the show users command in EXEC mode. show users

show history

Command Command Description Command Syntax show history To list the commands you have entered in the current EXEC session, use the show history command in EXEC mode. show history

show arp

Command Command Description Command Syntax show arp To display the entries in the Address Resolution Protocol (ARP) table, use the show arp privileged EXEC command. show arp

show protocols

Command Command Description Command Syntax show protocols Use the show protocols EXEC command to display the configured protocols. show protocols

interface serial 0/0

Command Command Description Command Syntax interface serial 0/0 Use the interface serial 0/0 global configuration command to configure an interface type and enter interface configuration mode. interface serial 0/0

ip address

Command Command Description Command Syntax ip address <ip address> <netmask> To set a primary or secondary IP address for an interface, use the ip address interface configuration command. To remove an IP address or disable IP processing, use the no form of this command. ip address ip-address mask [secondary]

clock rate 56000

Command Command Description Command Syntax clock rate 56000 To configure the clock rate for the hardware connections on serial interfaces such as network interface modules (NIMs) and interface processors to an acceptable bit rate, use the clock rate command in interface configuration mode. To remove the clock rate if you change the interface from a DCE to a DTE device, use the no form of this command. clock rate speed-in- bits-per-second

no shutdown

Command Command Description Command Syntax no shutdown To restart a disabled interface, use the no shutdown command. This restart will cause newly configured parameters, such as an IP address, to take effect. Perform this on all interfaces in use as they are shutdown by default. no shutdown

erase startup-config

Command Command Description Command Syntax erase startup-config The erase startup-config EXEC command erases or deletes the configuration pointed to by the CONFIG_FILE environment variable. If this variable points to NVRAM, the router erases NVRAM. If the CONFIG_FILE environment variable specifies a Flash memory device and configuration filename, the router deletes the configuration file. erase { filesystem : ¦ start-up config}

copy running-config startup-config

Command Command Description Command Syntax copy running-config startup-config The copy running-config startup-config command saves the running configuration to the startup configuration. This modifies the software configuration register boot field. copy {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp} {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp}

shutdown

Command Command Description Command Syntax shutdown Use the shutdown command to administratively disable an interface. If the interface is disabled no data will be passed through that interface. shutdown

interface fastethernet 0/0

Command Command Description Command Syntax interface fastethernet 0/0 The interface fastethernet command in global configuration mode selects a particular Fast Ethernet interface for configuration. interface type slot/port

description

Command Command Description Command Syntax description The description command in interface configuration mode allows the user to enter a comment about the interface. description string

banner motd # #

Command Command Description Command Syntax banner motd # # To specify a message-of-the-day (MOTD) banner, use the banner motd global configuration command. banner motd d message

clock timezone

Command Command Description Command Syntax clock timezone To set the time zone for display purposes, use the clock timezone global configuration command. To set the time to Coordinated Universal Time (UTC), use the no form of this command. clock timezone zone hours [minutes ]

ip host

Command Command Description Command Syntax ip host To define a static host name-to-address mapping in the host cache, use the ip host global configuration command. To remove the name-to-address mapping, use the no form of this command. ip host name-of-host [ tcp-port-number ] ip-address [ ip-address2 ... address8 ]

ip host

Command Command Description Command Syntax ip host To define a static host name-to-address mapping in the host cache, use the ip host global configuration command. To remove the name-to-address mapping, use the no form of this command. ip host name-of-host [ tcp-port-number ] ip-address [ ip-address2 ... address8 ]

copy running-config tftp

Command Command Description Command Syntax copy running-config tftp The copy running-config tftp command copies the running configuration file to a TFTP server. copy {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp} {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp}

copy tftp running-config

Command Command Description Command Syntax copy tftp running-config The copy tftp running config command copies a configuration file from a TFTP server to the running configuration. copy {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp} {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp}

show cdp neighbors

Command Command Description Command Syntax show cdp neighbors Use the show cdp neighbors command in the privileged EXEC mode to display information about directly connected Cisco neighbors. This is a Cisco proprietary command and will not recognize equipment from other vendors. show cdp neighbors [ type number ] [detail]

cdp run

Command Command Description Command Syntax cdp run To enable CDP, use the cdp run command in global configuration mode. To disable CDP, use the no form of this command. CDP is enabled by default at the global level and on each supported interface in order to send or receive CDP information. However, some interfaces, such as ATM interfaces, do not support CDP. cdp run

cdp enable

Command Command Description Command Syntax cdp enable Use the cdp enable in the interface configuration mode to enable CDP on an interface. cdp enable

clear cdp counters

Command Command Description Command Syntax clear cdp counters Use the clear cdp counters command in the global configuration mode to reset the traffic counters to zero. clear cdp counters

show cdp

Command Command Description Command Syntax show cdp Use the show cdp command in the privileged EXEC mode to display global CDP information, including timer and hold-time information. show cdp

show cdp entry device-name [protocol ¦ version]

Command Command Description Command Syntax show cdp entry To display information about a specific neighboring device discovered using CDP, use the show cdp entry command in privileged EXEC mode. show cdp entry {* ¦ device-name [*] [protocol ¦ version]}

show cdp interface [type number]

Command Command Description Command Syntax show cdp interface To displays information about interfaces on which CDP is enabled, use the show cdp interface command in the privileged EXEC mode. show cdp interface [type number ]

no cdp run

Command Command Description Command Syntax no cdp run To disable CDP, use the no cdp run command. CDP is enabled by default at the global level and on each supported interface in order to send or receive CDP information. However, some interfaces, such as ATM interfaces, do not support CDP. no cdp run

no cdp enable

Command Command Description Command Syntax no cdp enable Use the no cdp enable interface configuration command to disable CDP on an interface. CDP is enabled by default on all supported interfaces. no cdp enable

clear cdp table

Command Command Description Command Syntax clear cdp table To clear the table that contains CDP information about neighbors, use the clear cdp table command in privileged EXEC mode. clear cdp table

show cdp traffic

Command Command Description Command Syntax show cdp traffic To display the CDP counters, including the number of packets sent and received and checksum errors, use the show cdp traffic command in the privileged EXEC mode. show cdp traffic

show debugging

Command Command Description Command Syntax show debugging To display information about the types of debugging that are enabled, use the show debugging command in the privileged EXEC mode. show debugging

cdp holdtime

Command Command Description Command Syntax cdp holdtime To specify the hold time to be sent in the CDP update package, use the cdp holdtime command in the privileged EXEC mode. cdp holdtime

debug cdp adjacency

Command Command Description Command Syntax debug cdp adjacency To troubleshoot or monitor CDP neighbor information, use the debug cdp adjacency command in the privileged EXEC mode. debug cdp adjacency

debug cdp events

Command Command Description Command Syntax debug cdp events To troubleshoot or monitor CDP events, use the debug cdp events command in the privileged EXEC mode. debug cdp events

debug cdp ip

Command Command Description Command Syntax debug cdp ip To troubleshoot or monitor CDP IP information, use the debug cdp ip command in the privileged EXEC mode. debug cdp ip

debug cdp packets

Command Command Description Command Syntax debug cdp packets To troubleshoot or monitor CDP packet-related information, use the debug cdp packets command in the privileged EXEC mode. debug cdp packets

connect

Command Command Description Command Syntax connect To log in to a host that supports Telnet, rlogin, or local-area transport (LAT), use the connect command in EXEC command. connect [ ip-address ¦ hostname ]

telnet

Command Command Description Command Syntax telnet To log in to a host that supports Telnet, use the telnet command in user EXEC or privileged EXEC mode. telnet { hostname ¦ ip-address } [ port ] [ keyword ]

exit

Command Command Description Command Syntax exit Use the exit command to exit any configuration mode or close an active terminal session and to terminate the EXEC mode. exit

logout

Command Command Description Command Syntax logout To terminate an active Telnet session, use the logout command at the prompt of the device to which you are connected. logout

Ctrl-Shift-6, x

Command Command Description Command Syntax Ctrl-Shift-6, x To suspend a Telnet session, use the key sequence Ctrl-Shift-6, x. Ctrl-Shift-6, x

show sessions

Command Command Description Command Syntax show sessions To display information about open LAT, Telnet, or rlogin connections, use the show sessions command in EXEC mode. show sessions

session-limit

Command Command Description Command Syntax session-limit To set the maximum number of terminal sessions per line, use the session limit command in line configuration mode. To remove any specified session limit, use the no form of this command. session-limit session-number

resume

Command Command Description Command Syntax resume Use the resume command to resume a Telnet session. resume

traceroute (trace)

Command Command Description Command Syntax traceroute To discover the routes that packets will actually take when traveling to a destination, use the traceroute command in user EXEC or privileged EXEC mode. This command is sometimes referred to as "trace". However, on the router it is actually traceroute . traceroute destination [ protocol ]

ping

Command Command Description Command Syntax ping To diagnose basic network connectivity on Apollo, AppleTalk, Connectionless Network Service (CLNS), DECnet, IP, Novell IPX, VINES, or XNS networks, use the ping command in either the user or privileged EXEC. ping [ protocol ] { ip-address ¦ hostname

show ip route

Command Command Description Command Syntax show ip route To the display the current state of the routing table, use the show ip route command in the privileged EXEC mode. show ip route

boot system

Command Command Description Command Syntax boot system To specify the system image that the router loads at startup, use the boot system command in global configuration mode. If you configure the router to boot from a network server but do not specify a system image file with the boot system command, the router uses the configuration register settings to determine the default system image filename. boot system file-url

config-register

Command Command Description Command Syntax config-register To change the configuration register settings, use the config-register command in global configuration mode. config-register register-value

copy running-config tftp

Command Command Description Command Syntax copy running-config tftp The copy running-config tftp command copies the running configuration file to a TFTP server. copy {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp} {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp}

copy flash tftp

Command Command Description Command Syntax copy flash tftp To copy any file from a source to a destination, use the copy EXEC command. copy {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp} {flash ¦ ftp ¦ nvram ¦ running-config ¦ startup-config ¦ system ¦ tftp}

dir flash:

Command Command Description Command Syntax dir flash: Use the dir flash: command to examine the flash and look for a valid Cisco IOS® Software image. dir [/all] [filesystem : ¦file-url ]

boot flash:

Command Command Description Command Syntax boot flash: Command tells the router to boot the flash device. boot flash [ flash-fs : ] [partition-number : ¦ filename ]

confreg

Command Command Description Command Syntax confreg To change the configuration register settings while in ROM monitor mode, use the confreg ROM monitor command. confreg [ value ]

xmodem

Command Command Description Command Syntax xmodem To copy a Cisco IOS image to a router using the ROM monitor and the Xmodem or Ymodem protocol, use the xmodem ROM monitor command. xmodem [ -c ][- y ][- e ][- f ][- r ][- x ][- s ][ data-rate ] [ filename ]

tftpdnld

Command Command Description Command Syntax tftpdnld The tftpdnld command downloads a Cisco IOS software image from a LAN server to Compact Flash using TFTP. The following tftpdnld variables are optional: TFTP_VERBOSE—Print setting TFTP_RETRY_COUNT—Number of times that the ROM monitor retries ARP and ACK. TFTP_TIMEOUT—Overall timeout of the download operation in seconds. TFTP_CHECKSUM—Performs a checksum test on the image. FE_SPEED_MODE—Sets the Fast Ethernet speed and duplex mode After you specify the variables, you must re-enter the tftpdnld command. tftpdnld

set

Variable Variable Description set Sets environmental variables.

IP_ADDRESS

Variable Variable Description IP_ADDRESS IP address of router when in ROMmon mode.

IP_SUBNET_MASK

Variable Variable Description IP_SUBNET_MASK Subnet mask of router when in ROMmon mode.

DEFAULT_GATEWAY

Variable Variable Description DEFAULT_GATEWAY The default gateway of router when in ROMmon mode.

TFTP_SERVER

Variable Variable Description TFTP_SERVER The IP address of the TFTP server that router in ROMmon mode will download from.

TFTP_FILE

Variable Variable Description TFTP_FILE The file the router in ROMmon mode will download from the TFTP server.

ip route

Command Command Description Command Syntax ip route To establish static routes, use the ip route global configuration command. To remove static routes, use the no form of this command. ip route prefix mask { ip-address ¦ interface-type interface-number [ ip-address ]} [ distance ] [name] [permanent] [tag tag]

ip route 0.0.0.0 0.0.0.0 [next-hop-address ¦ outgoing interface]

Command Command Description Command Syntax ip route 0.0.0.0 0.0.0.0 [next-hop-address ¦ outgoing interface] To establish static routes, use the ip route global configuration command. To remove static routes, use the no form of this command. ip route prefix mask { ip-address ¦ interface-type interface-number [ ip-address ]} [ distance ] [name] [permanent] [tag tag]

|  | ip default-network Command Command Description Command Syntax ip default-network To select a network as a candidate route for computing the gateway of last resort, use the ip default-network global configuration command. ip default-network network-number |
| --- | --- |

show ip route

Command Command Description Command Syntax show ip route Use the show ip route EXEC command to display the current state of the routing table. show ip route [ address [ mask ] [ longer-prefixes ]] ¦ [ protocol [ process-id ]] ¦ [ list access-list-number ¦ access-list-name ]

router rip

Command Command Description Command Syntax router rip To configure the Routing Information Protocol (RIP) routing process, use the router rip global configuration command. router rip

network x.x.x.x

Command Command Description Command Syntax network x.x.x.x To specify a list of networks for a Routing Information Protocol (RIP), RIP version 2, or Interior Gateway Routing Protocol (IGRP) routing process, use this form of the network router configuration command. network network-address

bandwidth

Command Command Description Command Syntax bandwidth To set a bandwidth value for an interface, use the bandwidth command in interface configuration mode. The bandwidth command sets an informational parameter to communicate only the current bandwidth to the higher-level protocols. bandwidth kilobits

ip route-cache

Command Command Description Command Syntax ip route-cache Use the ip route-cache interface configuration command to control the use of high-speed switching caches for IP routing. To disable any of these switching modes, use the no form of this command. ip route-cache

no ip route-cache

Command Command Description Command Syntax no ip route-cache Use the ip route-cache interface configuration command to control the use of high-speed switching caches for IP routing. no ip route-cache

network network-number

Command Command Description Command Syntax network network-number To specify a list of networks for a Routing Information Protocol (RIP), RIP version 2, or Interior Gateway Routing Protocol (IGRP) routing process, use this form of the network router configuration command. network network-address

ip classless

Command Command Description Command Syntax ip classless At times the router might receive packets destined for a subnet of a network that has no network default route. To have the Cisco IOS software forward such packets to the best supernet route possible, use the ip classless global configuration command. To disable this feature, use the no form of this command. When this feature is disabled, the software discards the packets when a router receives packets for a subnet that numerically falls within its subnetwork addressing scheme. ip classless

no ip classless

Command Command Description Command Syntax no ip classless At times the router might receive packets destined for a subnet of a network that has no network default route. To have the Cisco IOS software forward such packets to the best supernet route possible, use the ip classless global configuration command. To disable this feature, use the no form of this command. When this feature is disabled, the software discards the packets when a router receives packets for a subnet that numerically falls within its subnetwork addressing scheme. no ip classless

ip split-horizon

Command Command Description Command Syntax ip split-horizon On by default, stops split horizon from occurring. ip split-horizon

no ip split-horizon

Command Command Description Command Syntax no ip split-horizon Allows routers to send updates out the same interface from which they came. no ip split-horizon

timers basic

Command Command Description Command Syntax timers basic Changes the holddown timer for routing updates, as well as other timers. timers basic

update-timer seconds

Command Command Description Command Syntax update-timer seconds Changes the update timer for the routing updates. update-timer seconds

show ip protocols

Command Command Description Command Syntax show ip protocols To display the parameters and current state of the active routing protocol process, use the show ip protocols EXEC command. show ip protocols

show ip interface

Command Command Description Command Syntax show ip interface To display the usability status of interfaces configured for IP, use the show ip interface EXEC command. show ip interface interface

debug ip rip

Command Command Description Command Syntax debug ip rip This command displays RIP transactions. debug ip rip

show ip rip database

Command Command Description Command Syntax show ip rip database Displays the contents of the RIP private database. show ip rip database [ ip -address { mask }]

show ip protocols

Command Command Description Command Syntax show ip protocols To display the parameters and current state of the active routing protocol process, use the show ip protocols EXEC command. show ip protocols {summary}

show ip interface brief

Command Command Description Command Syntax show ip interface brief To display a brief summary of the information and status for an IP address, use the show ip interface brief command in EXEC mode. show ip interface brief

passive interface

Command Command Description Command Syntax passive-interface The passive-interface command keeps a router from sending routing updates out an interface. passive-interface type number

maximum-paths

Command Command Description Command Syntax maximum-paths To control the maximum number of parallel routes an IP routing protocol can support, use the maximum-paths command in address family or router configuration mode. maximum-paths maximum

redistribute static

Command Command Description Command Syntax redistribute static To redistribute routes from one routing domain into another routing domain, use the redistribute router configuration command. To disable redistribution, use the no form of this command. redistribute protocol [process-id ] [metric metric-value ] [metric-type type-value ] [match {internal ¦ external 1 ¦ external 2 }] [tag tag-value ] [route map map-tag ] [weight weight ] [subnets]

router igrp

Command Command Description Command Syntax router igrp To configure the Interior Gateway Routing Protocol (IGRP) routing process, use the router igrp global configuration command. To shut down an IGRP routing process, use the no form of this command. router igrp autonomous-system

no router igrp

Command Command Description Command Syntax no router igrp To configure the Interior Gateway Routing Protocol (IGRP) routing process, use the router igrp global configuration command. To shut down an IGRP routing process, use the no form of this command. no router igrp autonomous-system

network

Command Command Description Command Syntax network To specify a list of networks for a Routing Information Protocol (RIP), RIP version 2, or Interior Gateway Routing Protocol (IGRP) routing process, use this form of the network router configuration command. To remove an entry, use the no form of this command. network network-address

no network

Command Command Description Command Syntax no network To specify a list of networks for a Routing Information Protocol (RIP), RIP version 2, or Interior Gateway Routing Protocol (IGRP) routing process, use this form of the network router configuration command. To remove an entry, use the no form of this command. no network network-address

ip route-cache

Command Command Description Command Syntax ip route-cache Use the ip route-cache interface configuration command to control the use of high-speed switching caches for IP routing. To disable any of these switching modes, use the no form of this command. ip route-cache

no ip route-cache

Command Command Description Command Syntax no ip route-cache Use the ip route-cache interface configuration command to control the use of high-speed switching caches for IP routing. To disable any of these switching modes, use the no form of this command. no ip route-cache

variance

Command Command Description Command Syntax variance To control load balancing in an IGRP-based internetwork, use the variance router configuration command. The variance value determines whether IGRP will accept unequal-cost routes. An IGRP router will only accept routes equal to the local best metric for the destination multiplied by the variance value. To reset the variance to the default value, use the no form of this command. variance multiplier

default-information originate

Command Command Description Command Syntax default-information originate To generate a default route into RIP, use the default-information originate router configuration command. To disable this feature, use the no form of this command. default-information originate [route-map mapname ]

ip default-network

Command Command Description Command Syntax ip default-network To select a network as a candidate route for computing the gateway of last resort, use the ip default-network global configuration command. To remove a route, use the no form of this command. ip default-network network-number

clear ip route *

Command Command Description Command Syntax clear ip route * This command removes all routes from the IP routing table. It can also be used to remove a specific route. clear ip route {network [mask ] ¦ * }

show running-config interface

Command Command Description Command Syntax show running-config interface Shows the running configuration for the specified interface. show running-config interface interface

show running-config ¦ begin interface

Command Command Description Command Syntax show running-config ¦ begin interface Begins the running configuration output at the specified interface. show running-config ¦ begin interface interface

show running config ¦ begin igrp

Command Command Description Command Syntax show running config ¦ begin igrp Shows the running configuration beginning at the specified routing protocol. show running config ¦ begin igrp

debug ip igrp events

Command Command Description Command Syntax debug ip igrp events Shows all IGRP events that are occurring debug ip igrp events

debug ip igrp transactions

Command Command Description Command Syntax debug ip igrp transactions Shows IGRP updates that are occurring between IGRP routers debug ip igrp transactions

debug ip packet

Command Command Description Command Syntax debug ip packet Use the debug ip packet EXEC command to display general IP debugging information. debug ip packet

ip route-cache interface configuration

Command Command Description Command Syntax ip route-cache interface configuration Use the ip route-cache interface configuration command to control the use of high-speed switching caches for IP routing. ip route-cache interface configuration

undebug all

Command Command Description Command Syntax undebug all Turns off all debugging undebug all

variance router configuration

Command Command Description Command Syntax variance router configuration To control load balancing in an IGRP-based internetwork, use the variance router configuration command. variance router configuration

no ip redirects

Command Command Description Command Syntax no ip redirects Disable ICMP redirects. no ip redirects

show ip rip database

Command Command Description Command Syntax show ip rip database To display summary address entries in the RIP routing database entries if relevant are routes being summarized based upon a summary address, use the show ip rip database command in EXEC mode. show ip rip database [ ip-address { mask }]

ping [protocol] {host ¦ address}

Command Command Description Command Syntax ping [protocol] {host ¦ address} Use the ping command in the privileged or user EXEC to diagnose basic network connectivity on Apollo, AppleTalk, Connectionless Network Service (CLNS), DECnet, IP, Novell IPX, VINES, or XNS networks. The optional protocol argument can be any of the following: apollo, appletalk, clns, decnet, ip, ipx, vines, or xns. To perform an extended ping, enter the ping command with no arguments. ping [ protocol ] { ip-address ¦ hostname }

debug telnet

Command Command Description Command Syntax debug telnet The telnet negotiation process can be viewed using the debug telnet command. debug telnet

clear counters

Command Command Description Command Syntax clear counters Many steps occur during the processing of a packet, and tests are performed at each step. The outcome of each step is recorded in an interface counter. Network administrators can analyze these interface counters to determine the reasons for sluggish router and network performance. The clear counters privileged EXEC command is used to set all the counters of the specified interfaces to zero. clear counters interface-type number

debug all

Command Command Description Command Syntax debug all To enable all system diagnostics, enter the debug all command in privileged EXEC mode. The no debug all command turns off all diagnostic output. Using the no debug all command is a convenient way to ensure that you have not accidentally left any debug commands turned on. debug all

terminal monitor

Command Command Description Command Syntax terminal monitor To display debug command output and system error messages for the current terminal and session, use the terminal monitor command in EXEC mode. terminal monitor

service timestamps debug uptime

Command Command Description Command Syntax service timestamps debug uptime To configure the system to time-stamp debugging or system logging messages, use one of the service timestamps commands in global configuration mode. To disable this service, use the no form of this command. service timestamps message-type [uptime] service timestamps {debug ¦ log} uptime service timestamps {debug ¦ log} datetime [msec] [localtime] [show-timezone] [year] no service timestamps [debug ¦ log]

ip http server

Command Command Description Command Syntax ip http server To enable the HTTP server on your system, including the Cisco web browser user interface, use the ip http server command in global configuration mode. To disable the HTTP server, use the no form of this command. ip http server

netstat

Command Command Description Command Syntax netstat The netstat command is used in Windows and UNIX/Linux to display TCP/IP connection and protocol information. netstat

access-list

Command Command Description Command Syntax access-list To define an access-control list, use the access-list global configuration command. To remove a standard access list, use the no form of this command. access-list access-list-number {deny ¦ permit¦ remark line} {any ¦ source [source-wildcard ]}[log]

ip access-group

Command Command Description Command Syntax ip access-group To control access to an interface, use the ip access-group command in interface configuration mode. To remove the specified access group, use the no form of this command. ip access-group access-list-number ¦ access-list-name {in ¦ out}

access-list access-list-number

Command Command Description Command Syntax access-list access-list-number To define an access-control list, use the access-list global configuration command. To remove a standard access lists, use the no form of this command. access-list access-list-number ¦ access-list-name

any

Command Command Description Command Syntax any Use the keyword any as an abbreviation for a source and source-wildcard of 0.0.0.0 255.255.255.255. access-list access-list-number {deny ¦ permit ¦ remark line} {any ¦ source [source-wildcard ]}[log]

host

Command Command Description Command Syntax host Use host source as an abbreviation for a source and source-wildcard of source 0.0.0.0. access-list access-list-number {deny ¦ permit ¦ remark line} {host ¦ source [source-wildcard ]} [log]

show access-lists

Command Command Description Command Syntax show access-lists Use host source as an abbreviation for a source and source-wildcard of source 0.0.0.0. To display the contents of current access lists, use the show access-lists privileged EXEC command. show access-lists [ access-list-number ¦ access-list-name ]

access-list access-list-number {deny ¦ permit} source [source-wildcard ] [log]

Command Command Description Command Syntax access-list access-list-number {deny ¦ permit} source [source-wildcard] [log] To define an access-control list, use the access-list global configuration command. To remove a standard access lists, use the no form of this command. access-list access-list-number {deny ¦ permit } source [ source-wildcard ] [log]

no access-list access-list-number

Command Command Description Command Syntax no access-list access-list-number To define an access-control list, use the access-list global configuration command. To remove a standard access lists, use the no form of this command. no access-list access-list-number ¦ access-list-name

Extended ACL Example

Command Command Description Command Syntax access-list 101 deny tcp 192.168.14.0 0.0.0.255 any eq 80 To define an extended IP access list, use the extended version of the access-list global configuration command. Extended ACLs check the source and destination packet addresses as well as being able to check for protocols and port numbers. access-list access-list-number [ dynamic dynamic-name [ timeout ]] { deny ¦ permit } protocol source source-wildcard destination destination-wildcard [precedence precedence ] [ tos tos ] [ log ¦ log-input ]

ip access-group access-list-number {in ¦ out}

Command Command Description Command Syntax ip access-group access-list-number { in ¦ out } To configure an access list to be used for packets transmitted to and from the host, use the ip access-group interface configuration command. To disable control over packets transmitted to or from a host, use the no form of this command. ip access-group access-list-number ¦ access-list-name { in ¦ out }

ip access-list

Command Command Description Command Syntax ip access-list IP named ACLs allow standard and extended ACLs to be given names instead of numbers. A named ACL is created with the ip access-list command. ip access-list { standard ¦ extended } name

access-class

Command Command Description Command Syntax access-class To restrict incoming and outgoing connections between a particular vty and the addresses in an access list, use the access-class command in line configuration mode. To remove access restrictions, use the no form of this command. access-class access-list-number { in ¦ out }